## Slide 1
Connecting and Testing Peripherals
Objective: Set up, connect, and thoroughly test peripheral devices like printers and webcams, ensuring proper communication with the computer operating system and resolving any connectivity or driver-level issues.

## Slide 2
Connecting and Testing a USB Webcam
Connect the Hardware: Plug the USB cable of your webcam into an available USB port on your computer.
Verification: Look for a power LED light on the webcam or a notification sound from Windows indicating a new device has been connected.
Install Drivers: Allow Windows to automatically install standard UVC (USB Video Class) drivers, or download specific drivers from the manufacturer's software site if required.
Verification: Open Device Manager, expand Cameras, and confirm the webcam appears without any yellow warning icons.
Test the Camera: Press the Windows key, type Camera, and open the default Windows Camera application.
Verification: Check that the app successfully displays your live video feed and click the capture button to take a test photo.

## Slide 3
Setting Up and Testing a Local Printer
Physical Connection & Power: Connect your printer via USB cable or ensure it is joined to the same local network, then turn it on using the power button.
Verification: Ensure the printer's status light or LCD screen remains steadily lit.
Install Drivers: Go to Settings > Bluetooth & devices > Printers & scanners, click Add device, or run the official driver installation software downloaded from the manufacturer's website.
Verification: Confirm the printer model appears listed under your system's installed printers.
Print a Test Page: Right-click the printer in Settings, select Printer properties, and click the Print Test Page button.
Verification: Check that physical paper feeds through the printer and prints the test page successfully.

## Slide 4
Simulating and Resolving a 'Printer Not Detected' Issue
Simulate Issue: Unplug the printer's USB cable from the computer to sever the hardware connection.
  Verification: Open Printers & scanners and notice the printer status change to offline or unreachable.
Reconnect Hardware: Plug the USB cable firmly back into a working USB port on the computer.
  Verification: Listen for the Windows hardware-connect chime.
Scan for Changes in Device Manager: Right-click the Start menu, open Device Manager, click on the top computer name or Action menu, and select Scan for hardware changes.
  Verification: Watch the device list refresh and verify that the printer reappears correctly without any missing driver alerts.

## Slide 5
Troubleshooting Webcam Not Working in Zoom (Working in Camera App)
Check App Permissions: Go to Windows Settings > Privacy & security > Camera, and ensure Let apps access your camera is turned On, and verify that Zoom is allowed in the app list.
  Verification: Confirm the toggle switch next to Zoom is enabled.
Release Conflicting App Locks: Close any other background applications (like Skype, Microsoft Teams, or open browser tabs) that might currently be using the webcam feed.
  Verification: Ensure no other program is actively locking the camera hardware.
Configure Zoom Video Settings: Open the Zoom desktop app, click your profile picture, go to Settings > Video, and check the Camera drop-down menu to ensure your physical webcam model is selected instead of a disabled or virtual camera option.
  Verification: Confirm your live video preview displays your image correctly inside Zoom.