## Slide 1
Here are 5 common issues users face with USB keyboards or mice on laptops, along with a practical solution for each:
Issue 1: The mouse or keyboard is completely unresponsive with no indicator lights.
  Solution: Unplug the USB cable or wireless receiver and plug it into a different USB port on your laptop to rule out a faulty port.
  Verification: Check if the optical LED sensor underneath the mouse or the indicator lights on the keyboard turn back on.
Issue 2: The cursor lags, stutters, or freezes intermittently.
  Solution: Replace low batteries (for wireless models) or clean dust and debris out from around the optical sensor lens on the bottom of the mouse.
  Verification: Move the mouse across a clean surface to ensure smooth, uninterrupted cursor tracking on screen.
Issue 3: Keystrokes are delayed or repeating multiple unexpected characters.
  Solution: Adjust the keyboard filter keys or repeat rate settings in the Windows Ease of Access / Keyboard settings panel.
  Verification: Type a quick test sentence in Notepad to confirm characters appear immediately and precisely once per press.
Issue 4: Windows displays a "USB Device Not Recognized" error pop-up.
  Solution: Uninstall the faulty device driver via Windows Device Manager and restart your laptop to force Windows to reinstall it automatically.
  Verification: Open Device Manager and verify that the yellow warning triangle next to the USB controller or input device disappears.
Issue 5: The wireless USB receiver drops connection frequently during use.
  Solution: Remove physical obstacles between the receiver and the device, or use a short USB extension cable to bring the receiver closer.
  Verification: Test the device close to the receiver to ensure a stable, drop-free connection.

## Slide 2
Here is a step-by-step troubleshooting flow to diagnose and resolve a Bluetooth headphones connection failure:
Step 1: Check Power and Activate Pairing Mode
Action: Turn on your Bluetooth headphones. If they are already on, power them off and turn them back on. Ensure they are in active Pairing Mode (usually by holding the power or dedicated Bluetooth button for 5 to 7 seconds).
Indicators to check: Look at the status LED indicator on the headphones. A rapid blinking light (often alternating between blue and red, or a pulsing white light) indicates that the headphones are discoverable.
Verification: Confirm you hear an audio cue from the headphones such as "Ready to pair" or "Pairing".
Step 2: Refresh Bluetooth on Your Phone
Action: Open your phone's Settings > Bluetooth (or swipe down to access the Quick Settings panel) and toggle the Bluetooth switch Off, wait 5 seconds, and toggle it back On.
Indicators to check: Ensure the Bluetooth icon in your phone's status bar is active and that the device list starts scanning/refreshing.
Verification: Check if your headphones' model name appears under the Available Devices or Other Devices section.
Step 3: Clear Interference and Check Battery Levels
Action: Ensure your headphones are charged (place them in their charging case for a few minutes if necessary) and move them within 1 meter of your phone, away from Wi-Fi routers or other heavy wireless equipment.
Indicators to check: Check the charging LED on the headphone case or body to ensure it is not displaying a low-battery red warning light.
Verification: Verify that the status LED stays lit without immediately turning off due to low power.
Step 4: Forget and Re-pair the Device
Action: If your headphones were previously paired but won't connect, go to Settings > Bluetooth on your phone, find your headphones under Paired Devices, tap the gear icon or info icon (i), and select Forget or Unpair. Then, initiate a fresh search and tap your headphone name to pair.
Indicators to check: Watch for a pop-up prompt on your phone asking to confirm the Bluetooth pairing request.
Verification: Confirm that the headphone status in your Bluetooth settings changes to "Connected for calls and audio" and the headphones play a "Connected" chime.
Step 5: Reset Headphone Network Settings (If Still Unresolved)
Action: Perform a hardware reset on the headphones (typically done by holding the power and volume buttons simultaneously for 10–15 seconds while placed in or out of the case, depending on the model).
Indicators to check: Watch for the status LED to flash red three times or reset its lighting pattern to factory defaults.
Verification: Open your phone's Bluetooth menu and attempt a fresh pairing process from Step 1.

## Slide 3
Webcam Not Detected During a Zoom Call (Windows 10 Checklist)
Physical Connection: Check that the webcam's USB cable is securely plugged straight into a working USB port on the PC.
  Verification: Look for a small power LED on the webcam body to light up.
Privacy Settings: Go to Settings > Privacy > Camera in Windows 10 and ensure that Allow apps to access your camera is turned On.
  Verification: Scroll down the list of apps and verify that the switch next to Zoom is also enabled.
App-Level Settings: Open Zoom, go to Settings > Video, and check the drop-down camera menu to ensure the correct physical webcam model is selected instead of a virtual camera.
  Verification: Confirm your live video preview box immediately displays your image.
Device Manager Check: Right-click the Windows Start button, open Device Manager, expand Cameras or Imaging devices, and check for any yellow warning icons.
  Verification: Verify the device status reads "This device is working properly."
Conflicting Applications: Close other background applications (like Skype, Teams, or browser tabs) that might be actively locking or using the webcam feed.
  Verification: Re-open Zoom video to see if the feed initializes without an error message.
Driver Update: If drivers are corrupt, right-click the webcam in Device Manager, choose Update driver, and select Search automatically for drivers.
  Verification: Ensure the device reinstalls successfully without errors.

## Slide 4
. Fixing a Printer Showing "Offline" Status Using Windows Troubleshooter
Launch the Troubleshooter: Open Windows Settings, navigate to Update & Security > Troubleshoot > Additional troubleshooters (or System > Troubleshoot > Other troubleshooters on newer builds), locate Printer, and click Run the troubleshooter.
  Verification: Watch the wizard window open and begin scanning your system for printing errors.
What Information the Tool Provides:
  It automatically checks if the printer is physically connected or reachable over the local network.
  It inspects the Windows Print Spooler service to see if it has crashed or stalled.
  It clears stuck, corrupted print jobs lingering in the print queue.
  It verifies whether the printer's status flag is incorrectly set to "Use Printer Offline" and attempts to toggle it back to online mode.
Apply Fixes: Follow any on-screen prompts provided by the wizard and click Apply this fix when recommended.
  Verification: Open Settings > Bluetooth & devices > Printers & scanners and confirm that the printer's status has changed from "Offline" back to "Ready".